## Slide 1: BY GROUP-14
TEAM MEMBERS:
Y. Eswar
M.Harshavardhan
C. Sridhar

## Slide 2: PROJECT DETAILS
PRESENTATION ON
INDUSTRIAL MONITORING SYSTEM

## Slide 3: ABSTRACT :
⯈
INDUSTRIAL MONITORING SYSTEM
This project mainly focuses on monitoring and controlling of Industrial Appliances remotely when the user is away from the place. Micro- controller is the core component of this project.
Objective of this project is to avoid number of accidents, human errors, and for manual safety.
As Human errors and manual safety systems lead to increase in industrial accidents, So here we are proposing a micro controller based industrial automation system that detects Smoke, Temperature, LPG Gas etc, to keep track of accidents, accordingly it on/off various load such as cooling fan, exhaust fan, water sprinkler and also it gives the information about detection to the supervisor through LCD Display.
This project includes the study of various electronic devices using sensors.

## Slide 4: INTRODUCTION :
Security is primary concern everywhere and for everyone. Every person wants his industry to be secured.
This project describes a security system that can monitor an industry. This is a simple and useful security system. Here our application uses Micro controller as its controller.
A Gas sensor is present to avoid leakage of liquid petroleum gas intimated with buzzer alert and simultaneously on the exhaust fan and switch off the lights automatically. This is very dangerous to human being present in the industry as it can cause fire.
Secondly a smoke sensor is present to detect if any person is smoking inside the industry entering in the industry as it gives probability of improper handling of equipment as well as it may cause risk of fire intimated with buzzer.
A temperature sensor is also present at this end to find out increase in temperature and switch on cooling fans to cool the room. In this way security is provided through all aspects.

## Slide 5: 8051 MICROCONTROLLER :
Micro-Controller is a small computer on a single integrated circuit. In modern technology, it is a System on a chip. A microcontroller contains one or more CPUs along with memory and programmable input-Output peripherals. There are two types of Microcontroller in use today; One is Embedded Microcontroller and Other is External Memory Microcontroller. External memory microcontroller is used when extra memory is required, therefore need can fulfilled by allowing the connection of external memory during the work as a separate ROM (RAM) which will make the work simpler and sophisticated. But in project hence memory required is within 8kb we are using embedded microcontroller.
Here we are using Atmel AT89S52 microcontroller. It is a powerful micro controller which provides a cost effective and highly-flexible solution to many embedded control applications. An embedded microcontroller is a chip which has a computer processor with all its support function, memory and input- output interfacing built into device.

## Slide 6: Features of AT89S52 Microcontroller :
Compatible with MCS-51 products
8k bytes of in-system programmable flash memory
Fully static operation from 0 Hz to 33 MHz
Three- level program memory lock 256 x 8-bit Internal RAM
4.0 to 5.5V operating range
32 programmable I/O lines
8 interrupt sources
Three 16-bit Timer/Counters
Low power idle and power -down modes

## Slide 7: FUNCTIONAL BLOCK DIAGRAM :

## Slide 8: CIRCUIT DIAGRAM

## Slide 9: COMPONENTS REQUIRED:
1. 8051 MICRO CONTOLLER
LCD Display
IR Sensor
Bluetooth Sensor
Buzzer
Touch Sensor
DST sensor
MQ-2 Sensor
HARDWARE COMPONENTS SOFTWARE COMPONENTS
1. KEIL SOFTWARE

## Slide 10: Code:
#include <reg51.h>
#include <intrins.h>
#define lcd P2
sbit rs=P0^0;
sbit rw=P0^1;
sbit en=P0^2;/P3^6/
char str;
char Charin=0;
void LCD_cmd(unsigned char);
void LCD_char(unsigned char);
void LCD_str(unsigned char *,unsigned char);
void delay_ms(unsigned int);
void LCD_init();

## Slide 11
void LCD_init(void){
LCD_cmd(0x38);//sets for
LCD_cmd(0x10);
LCD_cmd(0x01);
LCD_cmd(0x06);
LCD_cmd(0x0e);
}
void LCD_cmd(unsigned char cmd){
rw=0;
rs=0;
lcd=cmd;
en=1;
delay_ms(1000);
en=0;
}
void LCD_char(unsigned char ch)
{
rw=0;
rs=1;
lcd=ch;
en=1;
delay_ms(200);
en=0;}

## Slide 12
void LCD_str(unsigned char *s,unsigned char r){
unsigned char w;
for(w=0;w<r;w++){
LCD_char(s[w]);
delay_ms(100);
}
}
void delay_ms(unsigned int n){
unsigned int m;
for(n;n>0;n--)
for(m=121;m>0;m--);
nop();
nop();
nop();
}
sbit DHT11=P1^1;
sbit smoke=P1^3;
sbit red=P1^4;
sbit green=P1^6;
sbit buzzer=P1^7;
sbit IR=P1^2;
sbit touch =P1^5;

## Slide 13
unsigned char I_RH,D_RH,I_Temp,D_Temp,Checksum;
void delay_40us(){//each np is 1us
nop();nop();nop();nop();nop();
nop();nop();nop();nop();nop();
nop();nop();nop();nop();nop();
nop();nop();nop();nop();nop();
nop();nop();nop();nop();nop();
nop();nop();nop();nop();nop();
nop();nop();nop();nop();nop();
nop();nop();nop();nop();nop();
}
void request(){
DHT11=0;
delay_ms(18);
DHT11=1;
}
void response(){
while(DHT11==1);
while(DHT11==0);
while(DHT11==1);
}

## Slide 14
void request(){
DHT11=0;
delay_ms(18);
DHT11=1;
}
void response(){
while(DHT11==1);
while(DHT11==0);
while(DHT11==1);
}
unsigned char Receive_data()
{
unsigned char i,dataD=0;
for(i=0;i<8;i++){
while(DHT11==0);
delay_40us();
if(DHT11==1)
dataD=(dataD<<1)| (0x01);
else
dataD=(dataD<<1);
while(DHT11==1);
}
return dataD;}

## Slide 15
void delay(int time)
{
unsigned int i,j;
for(i=0;i<time;i++)
for(j=0;j<1275;j++);
}
void ser_int();
unsigned char rx();
void tx(unsigned char a);
void ser_int()
{
SCON=0x50;// Sets the serial control _register to enable serial reception
TMOD=0x20;//Configures the timer mode for the serial communication.
TH1=TL1=0xFD;//Sets the timer 1 high and low bytes for a specific baud rate
TR1=1;//Starts timer 1 to enable serial communication.
}

## Slide 16
unsigned char rx()
{
while(RI==0);//Waits until the receive interupt flag (RI) is set, indicating that there is _data to be read.
RI=0;//Resets the receive_interrupt flag.
return SBUF;//Returns the received byte from the serial buffer.
}
void tx(unsigned char a)
{
SBUF=a;// Places the byte 'a' into the serial buffer.
while(TI==0);//Waits until the transmit _interrupt flag (TI) is set, indicating that the buffer is ready for the next byte.
TI=0;//Resets the transmit _interrupt flag after transmission.
}
//2 for off the buzzer
//1 for the red led
//0 for the night times
//3 for reset mode
//4 for displaying the temperature and humidity and verifying.

## Slide 17
void main(){
extern unsigned char a,b,c,dd;
LCD_init();
red=0;
green=0;
smoke=0;
buzzer=1;//not work
touch=0;
ser_int();
LCD_cmd(0x80);
LCD_str("Welcome to zenesis",12);
LCD_cmd(0xc0);
LCD_str("Please enter code:",12);
while(1){
unsigned char gets;
gets=rx();
tx(gets);

## Slide 18
if(touch==1){
buzzer=1;}
if(gets=='0'){
while(1){
if(IR==0){
LCD_cmd(0x01);
LCD_cmd(0x80);
LCD_str("detected",8);
delay_ms(100);
buzzer=0;}else{
LCD_cmd(0x01);
LCD_cmd(0x80);
LCD_str("not detected",12);
delay_ms(100);
buzzer=1;}
if(smoke==1){
red=1;
green=0;}else{
red=0;
green=1;}
request();
response();
I_RH=Receive_data();
D_RH=Receive_data();

## Slide 19
I_Temp=Receive_data();
D_Temp=Receive_data();
Checksum=Receive_data();
if(I_Temp>30){
buzzer=0;
red=1;
green=0;
}
if(I_RH>50){
buzzer=0;
red=1;
green=0;}
}
}else if(gets=='1'){
red=0;
green=1;
LCD_cmd(0x01);
LCD_cmd(0x80);
LCD_str("Hii 1",12);
}else if(gets=='2'){
buzzer=1;
red=0;
green=1;}

## Slide 20
else if(gets=='3'){
LCD_cmd(0x80);
LCD_str("Welcome to zenesis",12);
LCD_cmd(0xc0);
LCD_str("enter code:",11);
delay_ms(100);
LCD_cmd(0xcd);
LCD_char(gets);}
else if (gets=='4'){
LCD_cmd(0x01);
LCD_cmd(0x80);
LCD_str("Humidity=",12);
LCD_cmd(0xc0);
LCD_str("Temperature=",12);
request();
response();
I_RH=Receive_data();
D_RH=Receive_data();
I_Temp=Receive_data();
D_Temp=Receive_data();
Checksum=Receive_data();
if(smoke==1){
red=1;
green=0;}

## Slide 21
else{ red=0;
green=1;
}
if((I_RH+D_RH+I_Temp+D_Temp)!=Checksum){
LCD_str("Error",5);
}
else{
a=(I_RH/10)+48;
b=(I_RH%10)+48;
LCD_cmd(0X89);
LCD_char(a);
LCD_cmd(0X8a);
LCD_char(b);
LCD_cmd(0X8b);
LCD_char('%');
c=(I_Temp/10)+48;
dd=(I_Temp%10)+48;
LCD_cmd(0xcc);
LCD_char(c);
LCD_cmd(0xcd);
LCD_char(dd);
delay_ms(300);}}}}

## Slide 22: CONCLUSION :
The project we have undertaken has helped us to gain a better perspective on various aspects related to our course of study as well as practical knowledge of electronic equipment and communication. The extensive capabilities of this system are what make it so interesting.
From the convenience of a microcontroller, a user is able to control industrial accidents, human errors and for manual safety. This makes it possible for the user that there are less accidents taking place in industry and people’s life or company growth is not in risk anymore.
The end product will have a simplistic design making it easy for users so that they can interact. This will be essential because of the wide range of technical knowledge that industries have.

## Slide 23: FUTURE ASPECTS :
The future implications of this project are very great by considering the amount of time and resources it saves. The project we have undertaken can be used as a reference or as a base for realizing a scheme to be implemented in other projects of greater level such as temperature updates, device synchronization, etc. The project itself can be modified to achieve a home automation system which will then create a platform for user to interface between himself and his household.
In future the system will be small box combining the micro-controller and GSM module. The hardware will be self contained and it cannot be prone to electric failure. This module will have its own encapsulated UPS and charging system

## Slide 24: INDIVIDUAL CONTRIBUTIONS :
Y. Eswar-Implemented the LCD display connection to the micro-controller and also connected IR sensor to the circuit , and also analyzed the code. And also connected the Touch Sensor.
M. Harshavardhan- Implemented the connection between DHT sensor to the micro-controller and read the values and also connected MQ-2 Sensor to the circuit.
C. Sridhar- Implemented the connection between Bluetooth to the micro-controller and also did the connection of buzzer to the circuit.

## Slide 25: THANK YOU